## Slide 1
1
School of Electronics Engineering (SENSE)
Project-I (2026)
Smart Glove for Real-Time Sign Language to Speech Translation
Student Name(s):
V A Sri Harsha – 23BLC1024, Samarth Sudeep Jagtap – 23BLC1033, Pavan U Kulkarni – 23BLC1038
Guide:
Dr. Venkatesan C, SENSE
Programme / School:
B.Tech — SENSE, VIT Chennai
Review & Date:
Review-II · 30.09.2026 (Wednesday)
Guide's Signature with Date
Signature: _____________________
Date: _________________________
Approval is mandatory before every review. After signing, scan this slide and keep the scanned copy as Slide 1 of the presentation.

## Slide 2
2
Introduction & Problem Recap
Problem recap
Existing glove systems classify one letter or gesture at a time, with a deliberate pause around it; natural signing has no pauses and no segment boundaries (co-articulation).
Real sentences mix fingerspelled names with whole-sign words freely, so the model must infer which mode it is in from the raw stream alone.
There is no public continuous, multi-signer flex + IMU corpus for ASL, so glove results are not reproducible or comparable across groups.
Reported accuracy is usually isolated-gesture and signer-dependent; the drop under continuous, signer-independent conditions is rarely published.
Core problem: turn an unsegmented 11-channel sensor stream into a correct English sentence, for a signer the model has never seen.
Objectives
Build reproducible hardware: 5 flex sensors + MPU-6050 + ESP32 glove with open BOM, wiring diagram, calibration routine and firmware.
Collect a continuous, multi-signer ASL dataset as raw flex + IMU, with isolated and sentence-level subsets and signer-disjoint splits.
Train a segmentation-free CNN → BiLSTM → CTC model that labels the whole stream with no hand-marked sign boundaries.
Decode mixed fingerspelling and lexical signs via lexicon-constrained beam search over one shared output vocabulary.
Convert gloss to fluent English: rule-based reordering baseline, then T5 / mBART fine-tuned on ASLG-PC12 if time allows.
Evaluate honestly: WER and BLEU on signer-independent splits, with isolated-gesture accuracy compared explicitly against continuous accuracy.
Refinements after Review-I feedback
Vocabulary fixed to a closed, realistic set — the 26 fingerspelled letters plus 20–40 lexical signs — rather than open-vocabulary ASL.
Per-signer calibration added to the capture pipeline after flex-sensor baseline drift was observed between wearers and across sessions.
Acquisition standardised to a fixed sampling rate with timestamped 11-channel frames, so windows are reproducible across recording sessions.
Recording protocol formalised before collection: scripted sentences for coverage plus free-form signing for natural co-articulation.

## Slide 3
3
Detailed Literature Review
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
1 | Zhang, Wang, Zhao & Yu (2019) | MyoSign: End-to-End Sign Language Recognition with Wearables — Proc. ACM IUI '19 | Myo armband (forearm EMG + IMU); multimodal CNN → BiLSTM trained end-to-end with CTC loss | 93.7% word and 93.1% sentence accuracy without manual segmentation. Gap: forearm EMG cannot resolve per-finger configuration; no fingerspelling mode.
2 | Zhang, Jing, Wang & Zhao (2022) | WearSign: Pushing the Limit of Sign Language Translation — Proc. ACM IMWUT, 6(1) | Encoder–decoder with intermediate gloss supervision over inertial + EMG wearables | Closes the gap between sensor signal and spoken-language grammar. Gap: same armband modality limitation; decoding overhead is heavy for an embedded target.
3 | PenSLR (2024) | PenSLR: Persian End-to-End Sign Language Recognition Using Ensembling — arXiv:2406.16388 | Glove with 5 flex sensors + 1 IMU; multi-model ensemble decoded with CTC, no pre-segmentation | Validates that 5 flex + 1 IMU carries enough information for continuous CTC decoding. Gap: Persian Sign Language, word level only, no fingerspelling channel.
4 | SpellRing (2025) | SpellRing: Recognizing Continuous Fingerspelling in ASL Using a Ring — arXiv:2502.10830 | Thumb-worn ring, acoustic sensing + IMU, CTC continuous decoding | 82.45% top-1 word accuracy over a 1,164-word set; CTC generalises to fingerspelling. Gap: fingerspelling only, no lexical-sign vocabulary.
5 | Nguyen Ngoc, Truong, Nguyen Duong, Nguyen & Phung (2026) | Multimodal Smart Glove for Sign Language Recognition Using Deep Learning — arXiv:2607.06996 | Glove with flex sensors + IMU plus a face camera; LSTM classifier deployed via TensorFlow Lite | Reports ~95% accuracy on an isolated-gesture set with on-device inference. Gap: isolated words only, no continuous decoding, and the camera reintroduces lighting and privacy constraints.
6 | IoT Assistive Glove (2024) | IoT-Enabled Assistive Glove for Real-Time Sign Language Translation — Int. J. Innovations in Science & Technology | 5 flex sensors + MPU-6050 on an Arduino Nano, CNN–RNN hybrid, results streamed over Wi-Fi | Demonstrates a low-cost wireless assistive glove pipeline. Gap: isolated ASL gestures only; no CTC, so the signer must pause between signs.
Themes: (a) end-to-end continuous recognition with CTC, (b) glove-based finger-level sensing, (c) fingerspelling-specific recognition.

## Slide 4
4
Detailed Literature Review (contd.)
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
7 | Wu, Sun & Jafari (2016) | A Wearable System for Recognizing ASL in Real-Time Using IMU and sEMG — IEEE J. Biomed. Health Informatics, 20(5) | Fusion of inertial and surface-EMG features with classical classifiers on a 80-sign vocabulary | Established that IMU + sEMG fusion outperforms either modality alone in real time. Gap: isolated signs, small vocabulary, signer-dependent evaluation.
8 | Ji, Wang, Miao, Fan & Ru (2023) | Dataglove for Sign Language Recognition via Wearable Inertial Sensors — Sensors, 23(15), 6693 | Purely inertial dataglove (no flex sensors) with deep classification of gesture segments | Shows inertial-only sensing can separate many gestures. Gap: without flex channels, handshapes with similar motion but different finger configuration are confusable; no continuous decoding.
9 | Hall-Effect Sensor Glove (2026) | Multi-Purpose Low-Cost Hall-Effect Sensor Glove for Sign Language Recognition — arXiv:2601.11539 | Magnetic Hall-effect transduction of joint angle in place of resistive flex sensors | Documents mechanical degradation of resistive ink under repeated bending as a reliability limit. Gap: still isolated-gesture level; motivates a calibration routine in our own flex-based design.
10 | Feng, Zhou, Huang, Luo & Wu (2023) | Design and Implementation of Gesture Recognition System Based on Flex Sensors — IEEE Sensors J., 23(24) | Flex-sensor circuit design, voltage-divider conditioning and gesture classification | Provides the signal-conditioning reference for our own voltage-divider front end. Gap: hardware-focused; no sequence modelling or sentence-level recognition.
11 | Wen, Zhang, He & Lee (2021) | AI-Enabled Sign Language Recognition and VR Bidirectional Communication Using Triboelectric Smart Glove — Nature Communications, 12, 5378 | Self-powered triboelectric sensing glove with deep-learning recognition and a VR interface | Explicitly frames single-gesture recognition as insufficient for daily communication. Gap: sentence-level recognition from a glove remains open.
12 | Umut & Kumdereli (2024) | Novel Wearable System to Recognize Sign Language in Real Time — Sensors, 24(14), 4613 | Real-time wearable recognition system evaluated across multiple signers | Reports the accuracy drop when the system meets signers outside the training set. Gap: confirms signer-independent evaluation is the weak point of the field.
Continued — glove and alternative-sensing literature that informs our hardware choice and its known failure mode.

## Slide 5
5
Detailed Literature Review (contd.)
No. | Author(s) & Year | Title / Source | Method / Approach | Findings & Research Gap
13 | Khan, Jin, Lee, Arzu, Dang, Nguyen, Choi & Moon (2025) | Deep Learning Approaches for Continuous Sign Language Recognition: A Comprehensive Review | Survey of continuous SLR architectures, alignment losses and evaluation protocols | Confirms CTC and encoder–decoder alignment as the standard approaches for unsegmented input. Gap: the surveyed continuous work is overwhelmingly vision-based, not glove-based.
14 | Chen, Yao & Hung (2026) | Real-Time Sign Language Interpretation via Customized Sign Language Gloves and Motion Retrieval | Customised sensing glove with motion-retrieval matching for real-time interpretation | Demonstrates low-latency interpretation from a custom glove. Gap: retrieval against stored templates does not model co-articulation in continuous signing.
15 | Valarmathi, Ghousiya Begum & Manoj (2026) | Wearable Glove: Sign Language Interpretation With AI-Enabled Finger-Mounted Sensors | Finger-mounted sensor array with an AI classification stage for interpretation | Reinforces finger-level sensing as the right granularity for handshape. Gap: interpretation reported at gesture level, without a mixed fingerspelling and lexical vocabulary.
16 | Graves, Fernández, Gomez & Schmidhuber (2006) | Connectionist Temporal Classification — Proc. ICML '06 | CTC loss for labelling unsegmented sequence data with recurrent networks | The foundational method our pipeline depends on: removes the need for frame-level alignment. Included as the methodological basis rather than as a recent result.
17 | Raffel, Shazeer, Roberts et al. (2020) | Exploring the Limits of Transfer Learning with a Unified Text-to-Text Transformer — JMLR, 21(140) | T5 text-to-text transformer pretraining and fine-tuning framework | Basis for the planned gloss-to-English stage fine-tuned on ASLG-PC12. Gap: not sign-specific; gloss-to-English for ASL remains low-resource.
Research gaps identified: no glove system decodes lexical signs and fingerspelling in one vocabulary; no public continuous multi-signer flex + IMU corpus exists; signer-independent accuracy is rarely reported.

## Slide 6
6
System Design & Architecture
ON-GLOVE — BUILT AND STREAMING
5 × Flex sensors
one per finger · voltage divider → ADC
MPU-6050 IMU
6-axis accel + gyro · I2C
ESP32
samples all 11 channels fixed rate + timestamps
Host capture
serial / BLE stream labelling utility
Dataset
26 letters + 20–40 words raw 11-channel frames
MODEL AND DECODING — REMAINING WORK
Preprocessing
calibration, filtering, normalisation, windows
1-D CNN
local handshape and motion features
BiLSTM + CTC
bidirectional context, no frame labels
Beam search
lexicon trie over one shared vocabulary
Gloss → English
rule-based, then T5 / mBART
Example — “my name is Maya” → unsegmented 11-channel stream → CTC gloss ME NAME M-A-Y-A → “My name is Maya.”
Green blocks are complete and validated at this review; grey blocks are the remaining 25%. The blank token in CTC absorbs transitions and co-articulation, so no sign boundaries are hand-marked.
Notes: Insert your architecture / block diagram here.

## Slide 7
7
Implementation Details
Modules developed and integrated
Sensing module — five resistive flex sensors in voltage-divider configuration, one per finger, plus an MPU-6050 mounted on the back of the hand; both fixed to the glove with custom mounts.
Firmware module (ESP32) — ADC sampling of the five flex channels and I2C acquisition of six IMU axes, merged into a single timestamped 11-channel frame at a fixed sampling rate.
Streaming module — serial / BLE transmission of frames to the host with no dropped or reordered frames observed over sustained recording sessions.
Host capture and labelling utility (Python) — records a stream, tags it with the class being signed, and writes raw sensor values, timestamps and labels to disk.
Dataset builder — organises recorded sessions into per-class folders with a manifest, ready for windowing and signer-disjoint splitting.
Algorithms implemented
Per-signer calibration — open-hand and closed-fist reference poses captured at session start; each flex channel is min–max normalised against its own baseline to absorb wearer and mounting variation.
Signal conditioning — moving-average smoothing on the flex channels and gravity-component handling on the accelerometer before normalisation.
Fixed-rate framing — timestamp-driven sampling loop so that window length in samples corresponds to a known duration, making windows reproducible across sessions.
Sliding-window segmentation — overlapping windows over the 11-channel stream, prepared as the input tensor format the CNN front end expects.
Label encoding — the 26 fingerspelled letters and the recorded lexical signs are mapped into one shared output vocabulary, so a single CTC output layer can emit either mode.
Model training (CNN → BiLSTM → CTC), lexicon-constrained beam search and the gloss-to-English stage are specified and scaffolded but not yet trained — see Challenges & Remaining Work.

## Slide 8
8
Implementation Details (contd.)
ESP32 firmware — fixed-rate 11-channel acquisition
const uint8_t FLEX[5] = {32, 33, 34, 35, 36};
const uint32_t PERIOD_US = 10000; // 100 Hz fixed rate
uint32_t next_us;
void loop() {
uint16_t flex[5];
for (uint8_t i = 0; i < 5; i++)
flex[i] = analogRead(FLEX[i]); // per-finger bend
int16_t ax, ay, az, gx, gy, gz;
mpu.getMotion6(&ax, &ay, &az, &gx, &gy, &gz); // 6-axis IMU over I2C
Serial.printf("%lu,%u,%u,%u,%u,%u,%d,%d,%d,%d,%d,%d\n",
micros(), flex[0], flex[1], flex[2], flex[3], flex[4],
ax, ay, az, gx, gy, gz); // timestamped 11-channel frame
next_us += PERIOD_US; // drift-free scheduling
while ((int32_t)(micros() - next_us) < 0) { }
}
Host-side preprocessing and shared vocabulary
def calibrate(flex, lo, hi):
"""Min-max normalisation from open/closed reference poses."""
return np.clip((flex - lo) / (hi - lo + 1e-6), 0.0, 1.0)
def windows(frames, win=100, hop=25):
"""Overlapping windows over the 11-channel stream."""
for s in range(0, len(frames) - win + 1, hop):
yield frames[s:s + win] # shape (win, 11)
# one shared vocabulary: blank + 26 letters + lexical signs
VOCAB = ["<blank>"] + list(string.ascii_uppercase) + LEXICAL_SIGNS
stoi = {tok: i for i, tok in enumerate(VOCAB)}
Why these two pieces matter
Drift-free scheduling on the ESP32 keeps the sampling interval constant, so a window of N samples always represents the same duration — without this, CTC sees inconsistent time scales between sessions.
Per-signer calibration is what makes signer-independent evaluation possible later: raw flex values differ between wearers, normalised values do not.
A single shared vocabulary with one CTC blank token is the mechanism that lets the model emit a letter or a whole sign from the same output layer.

## Slide 9
9
Results & Analysis (75%)
11 / 11
Channels streaming (5 flex + 6 IMU)
26
Fingerspelled letter classes recorded
20–40
Lexical sign classes recorded
75%
Of planned work complete
Dataset collected
Subset | Classes | Status
Fingerspelled alphabet | 26 letters (A–Z) | Recorded
Lexical signs | 20–40 whole-sign words | Recorded
Continuous sentences | Mixed letter + sign utterances | Protocol defined, collection in progress
Signer coverage | Multiple signers, signer-disjoint splits | Splits defined, not yet frozen
Exact sample counts, repetitions per class and total recording duration are read from the capture manifest and inserted here before the review.
Acquisition validated
All five flex channels respond monotonically to joint bend, with clearly separated value bands between the fully open and fully closed positions.
The MPU-6050 returns six axes over I2C in the same frame as the flex values, giving hand orientation and motion alongside handshape.
Frames arrive at a constant rate with monotonic timestamps; no dropped or reordered frames were observed across sustained recording sessions.
Static handshapes produce visually repeatable multi-channel signatures across repetitions and across sessions after calibration.
Per-signer calibration removes the baseline offset seen between wearers, so the same handshape maps to a similar normalised vector.
Notes: Add your results here — graphs, tables, screenshots or outputs.

## Slide 10
10
Results & Analysis (contd.)
Analysis at this stage
What these results establish: the sensing and capture layer is reliable enough to train on — channels are responsive, separable by handshape, stable across sessions, and consistently timed.
What they do not establish: no recognition accuracy is claimed yet. WER on continuous sentences, BLEU on gloss-to-English output, and the isolated-versus-continuous gap all require the trained model.
Those three numbers are the headline deliverables for Review-III; reporting them honestly, including the drop on unseen signers, is a stated objective of this project.
Notes: Add your results here — graphs, tables, screenshots or outputs.

## Slide 11
11
Challenges & Remaining Work
Challenges faced and solutions
Flex-sensor baseline drift — raw resistance varied between wearers and between sessions as the glove shifted. Solution: an open-hand / closed-fist calibration captured at the start of every session, with each channel min–max normalised against its own baseline.
Mechanical fragility of the resistive strips — documented in the literature as ink degradation under repeated bending. Solution: strain-relieved mounts so the sensor bends along its rated axis, plus a periodic recalibration check; sensor lifetime testing is planned.
Inconsistent sampling interval — a naive delay-based loop produced variable frame spacing, which would make windows represent different durations. Solution: drift-free timestamped scheduling in firmware at a fixed rate.
Noise on the analog channels — ADC readings jittered on long cable runs. Solution: shortened and secured wiring, stable supply, and moving-average smoothing before normalisation.
Labelling continuous recordings — there are no sign boundaries to mark in natural signing. Solution: the CTC formulation removes the requirement; only the utterance-level gloss sequence is recorded, not frame-level labels.
Remaining work (25%)
Complete the continuous sentence subset and freeze the signer-disjoint train / dev / test splits.
Train the CNN → BiLSTM → CTC model on the collected corpus, with augmentation (time warping, sensor noise, per-signer scaling) and hyperparameter search on dev signers.
Implement lexicon-constrained beam search over the shared vocabulary so fingerspelled runs resolve to valid words and names.
Build the gloss-to-English stage: rule-based reordering baseline, with T5 / mBART on ASLG-PC12 as a stretch goal.
Evaluate: WER and BLEU on signer-independent splits, plus the explicit isolated-versus-continuous comparison; assemble the demo and report.
Timeline for completion by Review-III (28.10.2026)
Week 1 (30 Sep – 06 Oct): finish continuous sentence recordings, freeze splits, publish the dataset manifest.
Weeks 2–3 (07 – 20 Oct): model training and tuning; first WER numbers on the dev signers.
Week 4 (21 – 27 Oct): constrained decoding, gloss-to-English baseline, signer-independent evaluation, demo and report.
Critical path: the continuous sentence subset. Training cannot start until those recordings and their gloss transcripts are complete.

## Slide 12
12
References
[1] Q. Zhang, D. Wang, R. Zhao, and Y. Yu, “MyoSign: Enabling end-to-end sign language recognition with wearables,” in Proc. 24th Int. Conf. Intelligent User Interfaces (IUI), Marina del Rey, CA, USA, 2019, pp. 650–660.
[2] Q. Zhang, J. Jing, D. Wang, and R. Zhao, “WearSign: Pushing the limit of sign language translation using inertial and EMG wearables,” Proc. ACM Interact. Mob. Wearable Ubiquitous Technol., vol. 6, no. 1, pp. 1–27, 2022.
[3] “PenSLR: Persian end-to-end sign language recognition using ensembling,” arXiv:2406.16388, 2024.
[4] “SpellRing: Recognizing continuous fingerspelling in American Sign Language using a ring,” arXiv:2502.10830, 2025.
[5] A. T. Nguyen Ngoc, T. P. Truong, T. A. Nguyen Duong, V. L. Nguyen, and M. D. Phung, “Multimodal smart glove for sign language recognition using deep learning,” arXiv:2607.06996, 2026.
[6] “IoT-enabled assistive glove for real-time sign language translation using machine learning,” Int. J. Innovations Sci. Technol., 2024.
[7] J. Wu, L. Sun, and R. Jafari, “A wearable system for recognizing American Sign Language in real-time using IMU and surface EMG sensors,” IEEE J. Biomed. Health Inform., vol. 20, no. 5, pp. 1281–1290, 2016.
[8] A. Ji, Y. Wang, X. Miao, T. Fan, and B. Ru, “Dataglove for sign language recognition of people with hearing and speech impairment via wearable inertial sensors,” Sensors, vol. 23, no. 15, art. 6693, 2023.
[9] “Design and implementation of a multi-purpose low-cost Hall-effect sensor glove for sign language recognition,” arXiv:2601.11539, 2026.
IEEE format. All references above are cited in the Detailed Literature Review slides.

## Slide 13
13
References (contd.)
[10] D. Feng, C. Zhou, J. Huang, G. Luo, and X. Wu, “Design and implementation of gesture recognition system based on flex sensors,” IEEE Sensors J., vol. 23, no. 24, pp. 31389–31398, 2023.
[11] F. Wen, Z. Zhang, T. He, and C. Lee, “AI enabled sign language recognition and VR space bidirectional communication using triboelectric smart glove,” Nature Communications, vol. 12, art. 5378, 2021.
[12] İ. Umut and Ü. C. Kumdereli, “Novel wearable system to recognize sign language in real time,” Sensors, vol. 24, no. 14, art. 4613, 2024.
[13] A. Khan, S. Jin, G.-H. Lee, G. Arzu, M. Dang, T. Nguyen, W. Choi, and H. Moon, “Deep learning approaches for continuous sign language recognition: A comprehensive review,” 2025.
[14] C.-H. Chen, C.-Y. Yao, and S.-H. Hung, “Real-time sign language interpretation via customized sign language gloves and motion retrieval,” 2026.
[15] R. Valarmathi, K. Ghousiya Begum, and R. D. Manoj, “Wearable glove: Sign language interpretation with AI-enabled finger-mounted sensors,” 2026.
[16] A. Graves, S. Fernández, F. Gomez, and J. Schmidhuber, “Connectionist temporal classification: Labelling unsegmented sequence data with recurrent neural networks,” in Proc. 23rd Int. Conf. Machine Learning (ICML), Pittsburgh, PA, USA, 2006, pp. 369–376.
[17] C. Raffel, N. Shazeer, A. Roberts, et al., “Exploring the limits of transfer learning with a unified text-to-text transformer,” J. Mach. Learn. Res., vol. 21, no. 140, pp. 1–67, 2020.
References [16] and [17] are methodological foundations (CTC loss and the T5 framework) rather than recent sign-language results.

## Slide 14
14
Thank You
Project-I (2026) · SENSE · VIT Chennai